## Slide 1: Dynamic modeling, robust control and contact estimation of soft robotics
Committee members:
Wenlong Zhang (advisor)
Hamidreza Marvi
Hyunglae Lee
Spring Berman
Thomas Sugar
A Doctoral Dissertation Proposal
Zhi Qiao

## Slide 2: Background

## Slide 3: Presentation Outline
Background and motivation
  Overview of pneumatic actuated soft arm
  Related work in model based dynamic control
  Research gaps and contributions
Preliminary work
  Data-driven model and robust controller for silicone actuator
  Augmented-rigid arm model and sliding mode controller for fabric-pillow-based SISO system
Summary and Future work
  Summary of the current work
  Future work for augmented-rigid arm model and sliding mode controller for fabric-pillow-based SISO system
  Future work for soft contact with environment using fabric-beam-based MIMO system
  Timeline

## Slide 4: Overview of soft arm design
  Having additional limbs has been a long dream for human beings
  The additional limb can help both healthy and impaired users
    Healthy user: holding multiple tools, extending reaching space
    Impaired user: grasping objects, detecting objects
  Compared with their rigid counterparts, soft arms shows advantages in:
    Compliance
    power-to-weight ratio
Copy rights: (Left) China News Service;(Mid) Marvel Entertainment, LLC;(Right) Lucasfilm Ltd. LLC;

## Slide 5: Overview of soft arm design
Prof. Ian Walker’s group (2004)
Prof. Darwin G. Caldwell’s group (2013)
Prof. Ian Walker’s group (2009)
Prof. Marc D. Killpack’s group (2015)
Prof. Daniela Rus’s group (2018)
Prof. Raffaello D’Andrea’s group (2019)
Notes: Jones cable,

## Slide 6: Related work in model-based dynamic control
Why soft system is hard to model?
  Nonlinear material properties
  Fabrication errors
Why not modeless control?
  Training data-set is large and consumes tons of time
  Performance is reduced when facing new and untrained environment
Why not high-dimensional finite element model-based control?
  High-dimensional requires lots of computational resources
  The performance doesn’t increase significantly when increase of the dimensions
Find a model that is low-dimensional but still can capture most of the dynamics of the system then design the controller on top of such model.

## Slide 7: Related work in model-based dynamic control
Prof. Ian Walker’s group (2010)
System dynamic model where G, B, E represents the effects of gravitational energy, potential energy due to bending and extension
Sliding model controller design
The error reaches the sliding surface in finite time and the state variables reach desired values exponentially fast.
Limitations:
  Assumes a backbone in the middle of the arm
  System uncertainties due to damping effect and input signal is not included
  No external disturbance estimation
Notes: Three cables were used to map from task space to joint space

## Slide 8: Related work in model-based dynamic control
System dynamic model where G, K, D represents the effects of gravitational energy, material spring and damper effects
Prof. Daniela Rus’s group (2020)
Curvature dynamic control with uncertainties
Limitations:
  Framework only works for backbone located at the centerline
  System uncertainties due to input signal is not included
  No estimation for external disturbance

## Slide 9: Related work in model-based dynamic control
System dynamic model (inverted pendulum)
Prof. Marc D. Killpack’s group (2015)
Limitations:
  The actuator needs to be specifically designed to fit the model requirements.
  Gravitational term is ignored
MPC controller design

## Slide 10: Limitations and objectives
Research gaps
  A backbone structure cannot cover the actuator without such feature
  The input uncertainty was not considered in the controller design
  External disturbance estimation is missing for CC assumption
Contributions
  Develop dynamic model for soft arm without backbone
  Develop robust controller for lumped disturbance rejection
  Develop disturbance estimator for contact event detection
“Dynamic modeling, robust control and contact estimation of soft robotics”

## Slide 11: Presentation Outline
Background and motivation
  Overview of pneumatic actuated soft arm
  Related work in model based dynamic control
  Research gaps and contributions
Preliminary work
  Data-driven model and robust controller for silicone actuator
  Augmented-rigid arm model and sliding mode controller for fabric-pillow-based SISO system
Summary and Future work
  Summary of the current work
  Future work for augmented-rigid arm model and sliding mode controller for fabric-pillow-based SISO system
  Future work for soft contact with environment using fabric-beam-based MIMO system
  Future work for multi-segments whole body grasping

## Slide 12: Insights from soft knee actuator
Pressure dynamics needs to be considered for fast movement
Actuator stiffness can be modeled as a function of chamber pressure
Experimental results. (Left) Pressure tracking (Right) Static characterization

## Slide 13: Contribution
Inspired from the soft knee actuator experiment, a linear parameter-varying (LPV) model for a silicone-based arm segment without backbone
H-infinity feedback controller combined with iterative learning control (ILC)
Experimental results

## Slide 14: Hardware Setup
Single chamber
One Segment
Multi-segment Arm
Nguyen, Pham Huy, et al. (2019)

## Slide 15: LPV Model
System parameters for bending and elongation motion are identified individually.
A mass-spring-damper model is identified
System is excited by a set of step inputs.
Control input and the elongation length is formed as an input-output-pair for MATLAB system identification toolbox.
Linear fit is applied to mass, spring and damper term with respect to operation point separately.

## Slide 16: Parameter Identification and Model Validation
System parameter identification for (Left) elongation motion (Right) bending motion
Model validation for (Left) elongation motion (Right) bending motion

## Slide 17: Feedback Controller Design
Closed-loop dynamics with fixed state-feedback gains ().
Robust controller to reject disturbances for all .
where is the range of control input.
Given , the deigned gains with can be achieved if there exist matrices and , such that the following LMI holds for all .
Feedback gain

## Slide 18: Combined Controller Design and Simulation
(Top) Simulation results
(Bottom) PD feedback and ILC controller
  Feedback controller
    Steady-state errors are observed in simulation (blue line)
  Introducing an iterative learning control (ILC) term
    Combine both feedforward and feedback term to achieve fast-tracking
    Application allows repeated moves
  Design of P-type ILC

## Slide 19: Experimental Results
Experimental results for (Top) elongation motion (Bottom) bending motion
  Key Findings
    The system shows large residual errors with PD-feedback controller Only (blue line).
    With ILC term, the system performance increased with iteration number N.
    Tracking errors are close to zero within 7 iterations.
  Limitations of the experiment
    Only small bending angle and elongation length scenario are tested.
    Deflation dynamics is not included.
    Simple mass-spring-damper framework cannot capture the full dynamics of the system.

## Slide 20: Presentation Outline
Background and motivation
  Overview of pneumatic actuated soft arm
  Related work in model based dynamic control
  Research gaps and contributions
Preliminary work
  Data-driven model and robust controller for silicone actuator
  Augmented-rigid arm model and sliding mode controller for fabric-pillow-based SISO system
Summary and Future work
  Summary of the current work
  Future work for augmented-rigid arm model and sliding mode controller for fabric-pillow-based SISO system
  Future work for soft contact with environment using fabric-beam-based MIMO system
  Timeline

## Slide 21: Limitations of Previous Work
Silicone material is heavy and stiff
Mass-spring-damper system accuracy is low
ILC cannot handle non-repetitive disturbance and noise
Lightweight fabric-pillow-based arm
Augmented-rigid arm model
Design sliding mode controller with disturbance observer for SISO system

## Slide 22: Contribution
Develop augmented-rigid arm model for fabric-pillow-based actuator without backbone
Design a baseline SMC method for SISO system path tracking
Design a disturbance observer to reduce the input chattering and estimate lumped disturbance

## Slide 23: Augmented-rigid Arm Model
MIT group:
  Backbone in the center
  Single chamber silicone actuator
Fabric-pillow-based arm:
  Hollowed in the center but with inextensible layer
  Serial connected pillow actuators
Prof. Daniela Rus’s group (2020)

## Slide 24: Kinematics with
The norm of indicates the distance between the CC layer (solid black) to the center line (dashed red).
is calculated using position feedback in task space

## Slide 25: Forward Kinematic Results
Experiment setup
  and is calculated from the motion capture position feedback
  Center of the tip is estimated from and using the proposed model
  Compare the estimation with actual measurement
Key findings
  Introducing improves the kinematic model performance
  The normalized estimation error is less than 1 percent
Experimental results. (Left) update rule
(Right) position errors in task space

## Slide 26: Dynamic Model with Parameter Uncertainties
System with bounded uncertainties
Full system dynamics
System Identification
  Excitation Signal
  Total trials: 30
  Trial duration: 30 sec
System ID results

## Slide 27: Baseline SMC Design
State space representation
Control input
Sliding surface
Reaching law
Stability proof

## Slide 28: Experimental Results
(Left) Multi-Steps (Right) Sum of sine waves
Experiment setup
  Multi-steps signal: Randomly selected in [-10,-40] degrees
  Sum-of-sines signal: frequency range [0.001,0.1] Hz
Key findings
  Baseline SMC method can track refence signal in both cases
  Input chattering needs to be reduced

## Slide 29: Presentation Outline
Background and motivation
  Overview of pneumatic actuated soft arm
  Related work in model based dynamic control
  Research gaps and contributions
Preliminary work
  Data-driven model and robust controller for silicone actuator
  Augmented-rigid arm model and sliding mode controller for fabric-pillow-based SISO system
Summary and Future work
  Summary of the current work
  Future work for augmented-rigid arm model and sliding mode controller for fabric-pillow-based SISO system
  Future work for soft contact with environment using fabric-beam-based MIMO system
  Future work for multi-segments whole body grasping

## Slide 30: Summary
Developed a LPV model together with ILC for a silicone-based actuator for fast and robust movement
In progress of augmented-rigid arm model and sliding mode controller for fabric-pillow-based SISO system
  Developed augmented-rigid arm model
  Designed baseline sliding mode controller
  Investigating the nonlinear disturbance observer for lumped disturbance estimation
  Preparing to submit the work to IEEE Robotics and Automation Letters in Jan. 2021

## Slide 31: Presentation Outline
Background and motivation
  Overview of pneumatic actuated soft arm
  Related work in model based dynamic control
  Research gaps and contributions
Preliminary work
  Data-driven model and robust controller for silicone actuator
  Augmented-rigid arm model and sliding mode controller for fabric-pillow-based SISO system
Summary and Future work
  Summary of the current work
  Future work for augmented-rigid arm model and sliding mode controller for fabric-pillow-based SISO system
  Future work for soft contact with environment using fabric-beam-based MIMO system
  Timeline

## Slide 32: Nonlinear Disturbance Observer
Assumptions
  Lumped disturbance is bounded
  The time derivative of the lumped disturbance is also bounded
  When contacting with environment, the external disturbance is dominant
Goals
  Reduce input chattering and estimate contact force
  Find proper gain matrix for NDOB
  Find proper candidate function to ensure the closed-loop system is stable

## Slide 33: Simulation and Experiments
Simulations
  Introduce constant external disturbances at time t and evaluate the convergence rate of the disturbance observer
Experiments
  A 6-axis force/torque sensor will be place on the path of the actuator movement
  Only tip will be in contact with the sensor
  A comparison between the estimated external disturbance and sensor measurement will be conducted.
6-axis force/torque sensor
Schematic figure of the experiment

## Slide 34: Presentation Outline
Background and motivation
  Overview of pneumatic actuated soft arm
  Related work in model based dynamic control
  Research gaps and contributions
Preliminary work
  Data-driven model and robust controller for silicone actuator
  Augmented-rigid arm model and sliding mode controller for fabric-pillow-based SISO system
Summary and Future work
  Summary of the current work
  Future work for augmented-rigid arm model and sliding mode controller for fabric-pillow-based SISO system
  Future work for soft contact with environment using fabric-beam-based MIMO system
  Timeline

## Slide 35: Limitations of Previous Work
Silicone material is heavy and stiff
Mass-spring-damper system is simple
ILC cannot handle non-repetitive disturbance and noise
System uncertainties is high
Actuation speed is slow
Performance drops significantly in low pressure
Fabric-beam-based Arm
Augmented-rigid Arm Model
Design SMCNDOB for MIMO system

## Slide 36: Insights from fabric-beam-based Arm
System uncertainties is low due to reduced chamber
Performance is better in low pressure due to the new fabric
More complex motion can be achieved with same module
Stretch sensor with IMU allows more sensory feedback and out-of-lab application

## Slide 37: Contribution
Develop augmented-rigid arm model for fabric-beam-based MIMO system in 3D space using local sensors
Design a baseline SMC method for MIMO system path tracking
Design NDOB for MIMO system and contact detection without force sensors.

## Slide 38: Kinematics model using stretch sensor and IMU
Unreliable
System dynamic model where G, K, D represents the effects of gravitational energy, material spring and damper effects
A fusion algorithm of pressure sensor, stretch sensor and IMU will be designed to map the task space to the joint space

## Slide 39: System ID for MIMO system
Experiment Setup
  Excitation Signal
  Total trials: 60
  Trial duration: 60 sec
MATLAB Grey-box system ID
  Assume both stiffness and damping matrix are diagonal matrix.
  Identify the parameters from each individual trial
  Find 95 percent confidence intervals of the parameters as the system parameter uncertainty bound
P_ctrl_2
Arm
P_ctrl_3
P_ctrl_1

## Slide 40: SMCNDOB, Simulation and Experiments
SMCNDOB for MIMO system
  Lumped disturbance is bounded
  The time derivative of the lumped disturbance is also bounded
  When contacting with environment, the external disturbance is dominant
Simulations
  Introduce constant disturbance at different direction and different time to evaluate the convergence rate of the disturbance observer.
Experiments
  Force/Torque sensor will be placed at different positions in the task space
  Only the tip is in contact with the sensor
  Results from the estimator and the sensor measurements will be compared.
6-axis force/torque sensor
Schematic figure of the experiment

## Slide 41: Presentation Outline
Background and motivation
  Overview of pneumatic actuated soft arm
  Related work in model based dynamic control
  Research gaps and contributions
Preliminary work
  Data-driven model and robust controller for silicone actuator
  Augmented-rigid arm model and sliding mode controller for fabric-pillow-based SISO system
Summary and Future work
  Summary of the current work
  Future work for augmented-rigid arm model and sliding mode controller for fabric-pillow-based SISO system
  Future work for soft contact with environment using fabric-beam-based MIMO system
  Timeline

## Slide 42: Timeline
(Jan. 2021). Dynamic model and control of a fabric-based SISO system. Target: IEEE Robotics and Automation Letters
(Jul. 2021). Soft contact with environment using fabric-beam MIMO system. Target: Soft Robotics
(Dec. 2021). Multi-segments whole body grasping for assisting human motion Target: TBD

## Slide 43: Refence
Jones, Bryan A., William McMahan, and Ian Walker. "Design and analysis of a novel pneumatic manipulator." IFAC Proceedings Volumes 37.14 (2004): 687-692.
McMahan, William, and Ian D. Walker. "Octopus-inspired grasp-synergies for continuum manipulators." 2008 IEEE International Conference on Robotics and Biomimetics. IEEE, 2009.
Best, Charles M et al. "Control of a pneumatically actuated, fully inflatable, fabric-based, humanoid robot." 2015 IEEE-RAS 15th International Conference on Humanoid Robots (Humanoids). IEEE, 2015.
Kang, Rongjie, et al. "Design, modeling and control of a pneumatically actuated manipulator inspired by biological continuum structures." Bioinspiration & biomimetics 8.3 (2013): 036008.
Della Santina, Cosimo, et al. "Dynamic control of soft robots interacting with the environment." 2018 IEEE International Conference on Soft Robotics (RoboSoft). IEEE, 2018.
Hofer, Matthias, Lukas Spannagl, and Raffaello D’Andrea. "Iterative learning control for fast and accurate position tracking with a soft robotic arm." Proc. IEEE/RSJ Int. Conf. Intell. Robots Syst.. 2019.
Kapadia, Apoorva D., et al. "A model-based sliding mode controller for extensible continuum robots." Proceedings of the 9th WSEAS international conference on Signal processing, robotics and automation. 2010.
Della Santina, Cosimo, et al. "Model-based dynamic feedback control of a planar soft robot: Trajectory tracking and interaction with the environment." The International Journal of Robotics Research 39.4 (2020): 490-513.
Nguyen, Pham Huy, et al. "Soft poly-limbs: Toward a new paradigm of mobile manipulation for daily living tasks." Soft robotics 6.1 (2019): 38-53.

## Slide 44
Thank you!