## Slide 1: Sliding mode control with nonlinear disturbance observer and state switch (SMCWNDOS)
Develop augmented-rigid arm model for fabric-pillow-based actuator without backbone
Design a baseline SMC method for SISO system path tracking
Design a disturbance observer to reduce the input chattering and estimate lumped disturbance
Experimental results for contact and no contact cases

## Slide 2: Augmented-rigid Arm Model
Fabric-pillow-based arm:
  Hollowed in the center but with inextensible layer
  Serial connected pillow actuators
The norm of indicates the distance between the CC layer (solid black) to the center line (dashed red).
is calculated using position feedback in task space

## Slide 3: Forward Kinematic Results
Experiment setup
  and is calculated from the motion capture position feedback
  Center of the tip is estimated from and using the proposed model
  Compare the estimation with actual measurement
Key findings
  Introducing improves the kinematic model performance
  The normalized estimation error is less than 1 percent
Experimental results. (Left) update rule
(Right) position errors in task space

## Slide 4: Dynamic Model with Parameter Uncertainties
System with bounded uncertainties
Full system dynamics
System Identification
  Excitation Signal
  Total trials: 30
  Trial duration: 30 sec
System ID results

## Slide 5: Baseline SMC Design
State space representation
Control input
Sliding surface
Reaching law
Stability proof

## Slide 6: Experimental Results
(Left) Multi-Steps (Right) Sum of sine waves
Experiment setup
  Multi-steps signal: Randomly selected in [-10,-40] degrees
  Sum-of-sines signal: frequency range [0.001,0.1] Hz
Key findings
  Baseline SMC method can track refence signal in both cases
  Input chattering needs to be reduced

## Slide 7: Nonlinear Disturbance Observer
Assumptions
  Lumped disturbance is bounded
  The time derivative of the lumped disturbance is also bounded
  When contacting with environment, the external disturbance is dominant
Goals
  Estimate contact force and detect contact event
  Stay compliant during the contact and recover back to desired path automatically
  Find proper candidate function to ensure the closed-loop system is stable

## Slide 8: Sliding mode control with nonlinear disturbance observer (SMCNDO)
Redesign control input
Design of NDOB
Stability proof
  Using and Assuming , the system is proved to be ultimately bounded in the sense of .
  The bounds are:
Bartle, R.G. and Sherbert, D.R., 2000. Introduction to real analysis (Vol. 2). New York: Wiley.
Corless, M. and Leitmann, G., 1981. Continuous state feedback guaranteeing uniform ultimate boundedness for uncertain dynamic systems. IEEE Transactions on Automatic Control, 26(5), pp.1139-1144.

## Slide 9: Experimental Results
Experiment setup
  Ramp rate: 1 rad/s
  No Object in the space
  Total of 5 trials
Key findings
  SMCNDO can track the desired path
  No saturation in chamber pressure

## Slide 10: Experimental Results
Experiment setup
  Ramp rate: 1 rad/s
  Object stay till 22 secs
  No further contact
  Total of 5 trials
Key findings
  SMCNDO can detect the contact
  Controller can track the path
  High estimated disturbance values
  Severe oscillation after contact ends

## Slide 11: Soft contact with SMCWNDOS
Assumptions
  the system always starts with no contact with the object
  The stiffness of the object is higher than the system and the object stays stationary during the contact.
  No further contact after the object is removed
Switch conditions
  Normal to Compliant: The estimated lumped disturbance and the tracking error goes beyond the threshold
  Compliant to Recovery: The estimated disturbance reduces below the threshold
  Recovery to Normal: The tracking error reduces below the threshold
Desired path augmentation:
  Normal: original path
  Compliant: current position
  Recovery: ramp path from the current position to the original path

## Slide 12: Experimental Results
Experiment setup
  Ramp rate: 1 rad/s
  Object stay till 22 secs
  No further contact
  Total of 5 trials
Key findings
  SMCWNDOS can detect the contact
  Controller can track the path
  Low estimated disturbance values
  Minimum oscillation after contact

## Slide 13: Evaluations of Experiments with Object
Averaged energy of the measured air pressures
Averaged root-mean-square error (RMSE) of position errors
Name | RMSE | 
SMC | 0.0251 | 46.5952
SMCNDO | 0.0422 | 56.2120
SMCWNDOS | 0.0236 | 47.5697
Name | RMSE | 
SMC | 0.0251 | 46.5952
SMCNDO | 0.0422 | 56.2120
SMCWNDOS | 0.0236 | 47.5697
Results
  SMC and SMCWNDOS shows similar performance when contact time is short.
  SMCWNDOS shows least RMSE values